## Slide 1: Module 2 Emission Reduction Quantification
Topic 4 Afforestation/Reforestation

## Slide 2: Acknowledgement
This presentation and accompanying materials was developed by Somerset Origination, as part of a programme overseen by the Gold Standard Foundation and funded by the German Ministry of Economic Affairs and Climate Action.

## Slide 3: Learning Objectives
To understand
The most used impact quantification methodologies
The emission reduction quantification
The baseline parameters
The project parameters
Notes: In this module we are going to learn about calculating emission reductions from a forestry projejct. By the end, you could understand:​​
​
The most used impact quantification methodologies​
The emission reduction quantification​
The baseline parameters​
The project parameters​
​
To help us understand all this, we will be following journey of the fictional carbon project developer, Carbon First. Carbon First has an idea to develop a Gold Standard forestry project and need to understand how they can calculate the emission reductions.​
​

## Slide 4: Methodologies
Single Methodology available
Methodology For Afforestation / Reforestation (A/R) GHGs Emission Reduction & Sequestration v2.1 (updated 16.05.2024)
Small number of projects
Notes: Under Gold Standard, only a single methodology is eligible to conduct Afforestation/Reforestation activities.
This makes Carbon First’s first decision easy.
Details of the methodology can be found of the GS SDG Impact Quantification Methodologies webpage, under the Afforestation/Reforestation subsection of Land-Use and Forestry & Agriculture.
In addition to the methodology, Carbon First needs to be sure to also download the latest version of the Land Use & Forests Activity Requirements.
When a methodology is reviewed and updated by GS, it receives a new version number. From a defined date, new projects will apply the new version of the methodology, while existing projects will continue on the version under which they were validated.
Those projects will switch to the new version when they enter a new crediting period.
Only 63 A/R VPAs are listed on the GS Registry, compared with over 2,000 cookstove VPAs
https://globalgoals.goldstandard.org/400-sdg-impact-quantification/
https://globalgoals.goldstandard.org/200-activity-requirements/

## Slide 5: Baseline Scenario
Notes: The baseline scenario is the most-plausible alternative land-use scenario that would occur without the implementation of the project. It serves as the reference against which the project's carbon emission reductions are measured.
For A/R projects, that involves understanding the current and potential future land-use options, in the absence of the project. The most-plausible scenario is dependent on a number of factors, such as grazing, wood harvesting, soil quality, and economic incentives.
The baseline scenario can be maintaining the current land-use (no change in biomass stocks) or a land-use change (resulting in an increase in biomass). Any decrease in biomass will be recorded as no change.
It is possible that different parcels of land may have different current and most-plausible alternative land use scenarios. In this case the project will need to be split into modelling units or strata, with each modelling unit assessed separately.
Carbon First assesses the baseline scenario of the project area and determines that the most plausible scenario is for half the site to remain as agricultural land, a quarter of the site to be barren land remaining as barren land, and the remaining quarter of the site to be converted from barren land to an open savannah, creating two separate modelling units.
Carbon First identifies that the area will not become forest without the project due the economic benefit of agriculture on half the site, and due to grazing and fuelwood extraction pressures for the other half
Carbon First conducts a baseline study following the A/R Methodology requirements to determine current and future baseline biomass stocks, as well soil management and inputs. With exact parameters described later on in this module.
This study is separate from any SDG Impact monitoring required (unless these impacts are derived from biomass changes).

## Slide 6: Project Scenario
Notes: Once the baseline scenario has been determined, Carbon First will now need to envisage the project.
The project scenario can have a range of approaches such as: Active Planting of trees, Assisted Natural Regeneration through indirect methods (i.e. excluding grazing), Timber plantations, Agroforestry, and Silvopasture.
Through a co-design approach with local communities, Carbon First determine the best approach is to create a mixed fruit and native tree conservation forest across most of the project area, providing a sustainable supply of food to local communities as well as enhancing local biodiversity.
The project will also reserve 20% of the agricultural area in the baseline for productive timber plantation, creating jobs and reducing some the economic impact of the lost agriculture.
Through the co-design process, local communities identify which type of trees they prefer and why, so that Carbon First can identify which species will be a lowest risk to be harvested in the future for the conservation forest, and which trees species may be most beneficial for the local community in the timber plantation.
Through this process, the project is expected to contribute to a range of SDGs, enhance carbon sequestration, and improve local livelihoods.
Carbon First must then continuously monitor the area for loss of trees, with monitoring and submission of tree growth being required at least every 5 years or less.

## Slide 7: Audience questions
Why is community engagement and participation key to an Afforestation/Reforestation project?
The community and local people may own, have rights over, live close to, or work on the land used in the project.
Considerations such as economic value of certain trees must be considered
Some trees may be more or less likely to be harvested for fuel or other purposes

## Slide 8: Baseline & Project Parameters
Notes: For both the baseline and project scenarios, Carbon First will need to determine the parameters for the Baseline and Project Scenarios.
Unlike other projects, the parameters measured in the Baseline and Project Scenarios, are largely the same.
Carbon First will be required to monitor Aboveground and Belowground Tree biomass for Baseline and Project calculations.
Aboveground and Belowground Non-tree biomass is then also required to be monitored in the Baseline scenario.
Finally, Soil Organic Carbon can be monitored in the Project scenario, and if so it must also be monitored in the Baseline scenario.
Under the GS Methodology, no Harvested wood, or Litter and dead wood is measured.
Leakage calculations also take into account Above and Belowground Leakage, but are calculated in a different way, covered in this module.

## Slide 9: Baseline & Project Parameters
Aboveground Biomass (tDM/ha) = SV x BEF x WD
Belowground Biomass (tDM/ha) = Aboveground biomass x R
Parameters required:
Stem Volume
Biomass Expansion Factor
Basic Wood Density
Root:Shoot Ratio
ABOVEGROUND BIOMASS
BELOWGROUND BIOMASS
Notes: In order to calculate Aboveground and Belowground Biomass Carbon First has to monitor a subset of parameters.
Stem volume (SV) refers to the total volume of the stems or trunks of trees in a modelling unit per hectare. This measurement is an essential parameter in forestry and carbon accounting, as it helps estimate the amount of biomass and carbon stored in the trees.
The Biomass Expansion Factor (BEF) is a multiplier used to estimate the total aboveground biomass of a forest from the stem biomass (or stem volume) alone. Since the stem biomass represents only part of a tree’s total biomass (which also includes branches, leaves, and sometimes roots), the BEF accounts for these additional components to provide a more comprehensive estimate of the total biomass of the trees.
Basic wood density refers to the mass of dry wood per unit volume, usually expressed in grams per cubic centimeter (g/cm³) or kilograms per cubic meter (kg/m³). It is a key parameter in forestry and carbon accounting because it helps estimate the total biomass of trees based on their volume.
The root-to-shoot ratio is the ratio of the biomass of a plant’s roots to the biomass of its aboveground parts (shoots), including stems, branches, and leaves.
Carbon First will need to monitor stem volume directly, whilst values for Biomass Expansion Factor, Wood Density, and Root:Shoot Ratio will typically utilise peer-reviewed or default values.

## Slide 10: Emission reduction calculations
Step 1. Calculate Baseline Removals
Step 2. Calculate Project Removals
Notes: Carbon First has now collected all the necessary information from each modelling unit in order to calculate the projects Emission Reductions.
All calculations are conducted at the Modelling Unit level until the final step.
To start, Carbon First calculates the Baseline Removals, by determining the total carbon stock in the baseline scenario, including non-tree biomass.
Soil carbon must also be included if monitored in the project scenario. If the baseline scenario is expected to increase in biomass, then the baseline value used in each subsequent year (t) must increase to reflect this.
After baseline removals have been calculated, next must Project Removals.
In order to calculate this, Carbon First must include the current carbon stocks for above and belowground biomass, as well as soil carbon if included.
These values will be derived from monitoring, however for ex-ante calculations, growth models and soil carbon stock change factors can be applied to estimate the potential project removals.
In addition, as Carbon First includes rotational forestry as the project scenario in one of their modelling units, the maximum Project Removals is limited by the Long-term average of Carbon Removals.
As shown by the graphs on the slides, this is the average carbon stock across the lifetime of a project.

## Slide 11: Audience questions
What monitoring techniques may be available for monitoring an Afforestation/Reforestation project?
Projects may choose a mix of field-based and remote monitoring
Field-based monitoring involves measuring tree stem on a sample
Digital monitoring uses satellite imagery

## Slide 12: Emission reduction calculations
Step 3. Calculate Leakage Emissions
Step 4. Calculate Other Emissions
Step 5. Calculate CO2 removal units
Step 6. Calculate total CO2 removal units
Notes: Once the baseline and project removals have been calculated, then additional emissions must also be calculated.
Due to the baseline scenario, it is likely the project will displace some agriculture and grazing, which will then move to other areas possibly causing deforestation, or preventing similar tree growth to occur. This is known as leakage.
Carbon First will need to account for this leakage by determining the amount of grazing and agriculture displaced (if any), this is called Activity Shifting.
There a multiple ways that activity shifting can be quantified, however they must use either a credible estimation, or representative survey to determine the degree of this activity shifting.
The activity shifting will then need multiplied by the expected tree above and belowground biomass stock in areas where the agriculture will move too - usually representative of the region the project takes place.
Leakage from grazing may be simpler, using livestock records to determine the number of livestock displaced and the grazing density.
In addition to leakage, Other Emissions may need to be calculated as well. These emissions include any usage of fertiliser as well as disturbance and burning from site preparation. Carbon First determine that none of these additional emissions need to be accounted for.
With Removals and Emissions accounted for, Carbon First can now calculate the removal units which will eventually be able to be issued as GSVERs.
Firstly at a modelling unit level, the Baseline Removals, Leakage Emissions, and Other Emissions are subtracted from the Project Removals, with this value (in tCO2/ha) then being multiplied by the planting unit area.
The final step, is then to sum all modelling units across all years up to the current year, in order to determine the current total Project removals.
Before Carbon First can then initiate the sale of these credits, they will have to consider that an additional 20% of credits will held in a risk buffer pool, which will be retired in case of any loss events such as a wildfire or other deforestation event.

## Slide 13: Q&A