## Slide 1: Module 4 Implementation, Monitoring and Reporting
Topic 4 Afforestation/Reforestation

## Slide 2: Acknowledgement
This presentation and accompanying materials was developed by Somerset Origination, as part of a programme overseen by the Gold Standard Foundation and funded by the German Ministry of Economic Affairs and Climate Action.

## Slide 3: Learning Objectives
To understand
The monitoring requirements of an Afforestation/Reforestation project
How to appropriately implement a monitoring plan
Notes: In this module we are going to learn about monitoring and reporting for a forestry project. By the end, you could understand:​​
​
The monitoring requirements of an Afforestation/Reforestation project
How to appropriately implement a monitoring plan
​
To help us understand all this, we will be following journey of the fictional carbon project developer, Carbon First. Carbon First has an idea to develop a Gold Standard forestry project and need to understand what they need to do to monitor the project’s ongoing performance.​
​

## Slide 4: Key Components of Monitoring
1) Data Available at Validation
2) Data Available at Verification
3) Monitoring Plan
BIOMASS EXPANSION FACTORS
WOOD DENSITY
SOIL CARBON STOCK
TREE GROWTH RATE
Notes: Carbon First are putting together their monitoring plan and collecting data for the ex ante calculations.
They need to determine:
What parameters are fixed, such as baseline land-use parameters (except where biomass increases in the baseline), and values for wood density, Biomass Expansion Factors, and Root to Shoot Ratios. Much of these are default values!
Parameters that need to be monitored ex-post, and estimated ex-ante for the purpose of calculating GSVERs; and
Develop a Monitoring plan to capture all required data in line with the methodology.

## Slide 5: Project Stratification
Project is divided into Modelling Units based on:
Baseline Scenario
Project Activity
Soil Conditions
Notes: When designing the monitoring plan, Carbon First will first need to take into account the stratification of the project into modelling units.
Each modelling unit is expected to have homogeneous characteristics, such as soil quality and condition, baseline land use and carbon stocks, and project carbon stocks.
It may be that more modelling units have be created as the project continues due to variations in growth (as well as any biomass losses) throughout the project area.
Through the previous modules Carbon First has identified at least 4 modelling units:
Agriculture remaining Agriculture, being converted to Conservation Forest through Active Planting
Agriculture remaining Agriculture, being converted to Rotational Forest through Active Planting
Barren Land remaining Barren Land, being converted to Conservation Forest through Active Planting
Barren Land transitioning to Savannah, being converted to Conservation Forest through Active Planting
For each identified modelling unit, a separate set of statistically significant parameters will need to monitored and measured.

## Slide 6: Key Survey Guidance
Notes: A/R Project Monitoring is complex
Gold Standard recommends following the Sourcebook for Land Use, Land-use Change and Forestry Projects.
This sourcebook is designed to be a guide for developing and implementing land use, land-use change and forestry (LULUCF) projects that meet the requirements for the Clean Development Mechanism (CDM) of the Kyoto Protocol.
It covers concepts such as additionality, baseline, leakage and permanence, and how to monitor, measure and analyse the parameters!
Carbon First follow the Sourcebook for guidance on things such as determining the sample approach, calculating the number of Plots required, and measuring key variables.
https://winrock.org/wp-content/uploads/2016/03/Winrock-BioCarbon_Fund_Sourcebook-compressed.pdf

## Slide 7: Audience questions
What are the key components of monitoring Afforestation/Reforestation project?
The growth and survival rate of the trees!
Including:
  Biomass expansion factor
  Wood density
  Tree growth rate
  Soil carbon stock

## Slide 8: Monitoring Plan
1. Consider Plot Design
A) B) C) D)
2. Determine Sample Size
3. Selecting Sampling Points
Notes: Carbon First are putting together their monitoring plan to be validated in the PDD and executed during the project!
They consider:
What are the methodological requirements?
What data must be collected?
What is the sampling requirements?
Most parameters they measure are collected using sampling plots, so first they must determine their plot design and size. There are multiple ways in which this can be conducted with a few examples as follows: A) Nested Square Plots
B) Nested Circular Plots
C) Transect Plots
D) Un-nested Plots
Variable or mixed plot approaches are also possible.
Each plot design has their strengths and weakness, such as nested plots which allow for more rapid assessments by increasing the minimum dbh of trees to be measured as the plot size increase, or transect plots which allow for information gathering across a gradient, or when site access may be an issue. When determining plot design, work with forestry experts to determine which is the best approach.
Carbon First has decided to use a circular nested plot design that has a radius of 20m, and now needs to estimate how many sample plots are required. Using a standard equation (shown on the slide), where N represents total number of possible plots, E represents the allowable error, t the t-distribution at 95% CL, and s the standard deviation of the primary variable (in this case aboveground biomass stock), with h denoting the separate strata. Standard deviation can be estimated through peer-reviewed data, or a pilot study.
Using this equation Carbon First determine that 29 plots are required to fulfil the sampling requirements.
Project Developers can utilise Sampling Calculators or create their own.
Finally, Carbon First determines where these plots will be located. Whether through random or stratified sampling (or other approaches), it is possible that restrictions it terms of access can be developed to ensure that access to all these points is reasonable for time and safety purposes. Through sampling Carbon First generates 29 random and accessible GPS from which the plots will originate from.
Carbon First also want the project to be a success and for the end users to benefit from the technology! They plan for monthly visits to sites to assess tree survival, and may even use drones to do so and hold continuous community events!
They decide to document every activity. This is helpful to demonstrate compliance to the VVBs and also to tell the story to the world!

## Slide 9: Monitoring Plan
Additional Baseline Monitoring
  Non-tree Biomass
Soil Carbon Cores
Permanent Plots vs Full Replacement
Local Expert is Key!
Notes: Sampling and monitoring between the baseline and project is mostly similar.
A key difference is the requirement to also monitor non-tree biomass. This primarily done through a quadrat approach, where by quadrats (generally between 3-5 per plot) are randomly distributed throughout the plot. Destructive sampling, such as the harvesting and drying in an oven, or non-destructive, such as regression equations derived from ground cover and sward height (among others), can be used.
Additionally, Soil Carbon monitoring, if required by the project and not using published literature, will need to include coring, where soil cores taken to a predetermined and consistent depth are taken using an augur, and then process in a laboratory (or equivalent field kit) to determine soil organic carbon content (among other possible variables). The number of soil cores is generally consistent with the number of non-tree biomass quadrats.
Carbon First also needs to decide where subsequent sampling events will take place. Options include Permanent Plots, where the same plots are monitored, to full replacement, where a new sample is developed, to a continuum in between.
Most importantly for GS A/R Projects is that plot design and monitoring can be highly variable, and as long as statistically significant measurements are produced it is recommended that Project Developers work with local forestry experts who can design an approach suitable for the ecosystem and characteristics of the area!
Carbon First decides that destructive sampling is most appropriate for the project in coordination with a local expert, due to lack of established regression equations, and that full replacement of plots will be used, primarily to allow for a greater area to be monitored over the course of the project.

## Slide 10: Data Collection
Tree Height (m)
Tree Diameter at Breast Height (cm)
Soil Organic Carbon (kgC/cm3)
Notes: Tree height is often considered a variable parameter in carbon sequestration projects, especially in afforestation, reforestation, and forest management activities. it keeps on increasing/changing during the crediting period. Tree height is generally measured with an inclinometer.
Tree diameter (typically measured as Diameter at Breast Height, or DBH, typically 1.3m) is a variable parameter in carbon sequestration and forestry projects. It keeps on increasing/changing during the project crediting period. Measured using DBH tape, varied approaches based on tree shape (seem diagram on slide)
Soil Organic Carbon is measured by analysing a soil core in a laboratory to determine Soil Organic Carbon Content.

## Slide 11: Audience questions
Why are local experts important for monitoring an Afforestation/Reforestation project?
Local knowledge
Build and conduct field monitoring plan
Compliments remote/digital monitoring

## Slide 12: Remote Sensing
Not currently permitted under methodology
Types
Satellite Imagery
LiDAR (Light Detection and Ranging)
Drone Imagery
Uses
Current and Historic Land Use
Evidence
Improved Data accuracy
Monitor health and survival
Notes: In combination with field monitoring Carbon First chooses to use remote sensing as a way to support the field data, as well as reduce monitoring costs.
Remote Sensing can be conducted via:
Satellite Imagery
LiDAR
Drone Surveys
Remote sensing can be used in a number of ways:
Identify current and historic Land Use
Evidence A/R activities
Extrapolate field data for greater accuracy of biomass estimates
Monitor tree health and survival
By using remote sensing Carbon First is able to add a premium to the credit price as investors have greater confidence in the ability of the project to ensure tree survival is as high as possible, and that any losses are correctly and transparently monitored.!
Please note that purely remote sensing-based monitoring approaches are currently not allowed under Gold Standard – but hybrid digital approaches combining remote sensing and on the ground calibration are being piloted.

## Slide 13: Reporting
Two main documents for reporting –
(i) Monitoring Report & (ii) Annual Report
Must Follow GS4GG Template
Supporting documents must accompany Monitoring Report
Must Follow Reporting Frequency
Validated or Verified by GS4GG accredited Third Party Auditor (Validation and Verification Body; VVB)
Notes: Monitoring Report - A monitoring report is a crucial document that provides a comprehensive summary of the project’s performance in terms of emissions reductions, carbon sequestration, and contributions to sustainable development goals.
Annual Report - Transparent, annual update reports need to be provided for Projects that have achieved the Project Design Certification stage or have successfully transitioned to Gold Standard for the Global Goals. An annual report shall be submitted for each monitoring year by end of next calendar year for which verification is not completed2. If a verification is in progress but not completed, then an Annual Report is still required by the end of calendar year.
All project reporting must be conducted using the Gold Standard (GS) prescribed template. The template is designed to capture all necessary details, including emissions reductions, sustainable development impacts, and monitoring data, in a structured format. By adhering to the prescribed template, project developers can streamline the review process, facilitate transparency, and ensure that all required information is provided in an organized and accessible manner.
Reporting Frequency deadlines in GS4GG:
(a) Agriculture specific: The first Verification Report shall be completed either
within two years of project start date or Project Design
Certification, whichever is later.
(b) A/R specific: Verification Report shall be completed at least every 5
years until the end of the crediting period.
VVB - The VVB is directly appointed by the Project Developer. A VVB shall be selected from the list of approved VVBs, eligible for the project type and pathway proposed. Validation and Verification Body (VVB) plays a critical role in conducting the performance review of a project. VVBs are accredited third-party organizations responsible for validating a project’s design and verifying its actual performance in terms of emissions reductions, carbon sequestration, and sustainable development contributions.

## Slide 14: Q&A